## Slide 1: Lattice Boltzmann method: Let’s suit up! Part I
Alessandro De Rosis
Lecturer in Virtual Engineering
Department of Mechanical, Aerospace and Civil Engineering (MACE)
The University of Manchester

## Slide 2
Lattice Boltzmann method (LBM): what is it?
Hands-on session
Outline
2

## Slide 3
Lattice Boltzmann method (LBM): what is it?
Hands-on session
Outline
3

## Slide 4
The 10-orders-of-magnitude hierarchy
Microscopic
Kinetic
Macroscopic
Time scale [s]
Length scale [m]
100
10-3
10-6
10-9
10-2
10-3
10-4
10-5
10-6
10-7
10-8
10-9
Finite difference method
Finite volume method
Element free Galerkin
Dissipative particle dynamics
Lattice Boltzmann method (LBM)
Off-lattice Monte Carlo
Molecular dynamics
4
v
v
Numerical simulations of fluid dynamics

## Slide 5: Lattice Boltzmann method
Lattice
Boltzmann
(Kinetic theory)
5

## Slide 6
Navier-Stokes equations…
Why LBM?
6

## Slide 7
ADVANTAGES
No moving meshes
Nonlinearity is local, nonlocality is linear
Easy implementation
Navier-Stokes equations…
…Boltzmann equation
Why LBM?
6

## Slide 8
Screenshot 2021-07-15 at 17.48.29
ADVANTAGES
No moving meshes
Nonlinearity is local, nonlocality is linear
Easy implementation
Increasing recognition from academia and industry
Scopus
Navier-Stokes equations…
…Boltzmann equation
Documents per year
Why LBM?
6

## Slide 9
Screenshot 2021-07-15 at 17.48.29
ADVANTAGES
No moving meshes
Nonlinearity is local, nonlocality is linear
Easy implementation
Increasing recognition from academia and industry
Suited for complex physics
Scopus
Navier-Stokes equations…
…Boltzmann equation
Documents per year
Why LBM?
6

## Slide 10: Multiphysics modelling by LBM
Fluid-structure interaction
Multiphase/component flows
Liquid jet break-up
Saito, De Rosis et al. (2018) Phys Rev E Kaleidoscope
Flapping wings
De Rosis et al. (2014) J Fluids Struct
3D MHD vortex: electric current
De Rosis (2017) Phys Rev E Kaleid.
Temporal jet at Re=3200, Sc=5
Turbulence & Magnetohydrodynamics
7
THEORY OF LBM & NUMERICAL SIMULATIONS
Fluid: LBM
Solid: FEM
IBM
Varicose break-up
Atomisation

## Slide 11
Why here?
How: from theory to implementation
LBM at UoM
Research groups and activities at MACE:
Modelling and Simulation Centre
LUMA & GASCANS
Thermofluids group
Microsystems group
SPHERIC: SPH vs LBM
Other institutions at UoM:
Computer Science
Biological Sciences
Chemical Engineering and Analytical Sciences
Biology Medicine and Health
Cell-Matrix research centre
Multiphysics modelling by LBM
Methodology
Applications
Biophysics
Energy &
mechanics
Improving accuracy and stability
Coding
HPC, GPU
GUI, pre- & post-proc
Beyond the Navier-Stokes equations
9
Nucleate pool boiling
Fluid-structure interaction
National and international network
UKCOMES
École Centrale de Lyon
Universitè de Genève
New Jersey Institute of Technology
University of Tsukuba
Other academic and industrial partners
De Rosis & Tafuni (2022)
Comput Aid Civ Inf

## Slide 12
LBM at UoM: our group today
9
Maryam Fatehifar (PhD student)
Multicomponent flows
Ruizhi Liu (PhD student)
Advanced LBMs
Yang Zhou (PhD student)
Boiling
Gabriela Lopez Santana (PhD student)
Cardiovascular flows
ADR (Lecturer)
Multiphysics modelling
Alistair Revell (Professor)
LBM, LUMA, turbulence, aerodynamics
Marta Camps (PDRA)
LUMA, Coupling with FVM
Rong Wang (PhD student)
Atmospheric flows and wind farm
Ian Hinder (Res Soft Eng)
FSI on GPUs

## Slide 13
Macroscopic and microscopic scales
16
At the macroscopic level, a fluid is a continuous material with some properties and it obeys the Navier-Stokes equations. Pressure, density and velocity are continuous variables which can be measured.
Linking macro and micro worlds

## Slide 14
Macroscopic and microscopic scales
16
At the microscopic level, we play another game. Here, the fluid is an ensemble of molecules with an unpredictable (chaotic) behaviour and it loses its apparent global coherence. The apparent continuity of the fluid is broken.
Establishing the link between macro and micro worlds is instrumental to a better understanding of the fluid behaviour.
Linking macro and micro worlds

## Slide 15
Macroscopic and microscopic scales
16
At the macroscopic level, we can visualise and measure density and velocity.
At the microscopic level, how can we define density and velocity while molecules move in a disordered way?
Linking macro and micro worlds

## Slide 16
Density and velocity at the microscopic scale
16
Particles move in an apparent disordered and random manner.
However, this apparent chaos hides info about the macroscopic properties.
Density is easy to get:
: number of particles
: mass of a particle
: control volume
For the velocity, we assume isotropy: the velocity vector of a particle can point in any direction with the same probability.
The average velocity magnitude is
Temperature should be considered.
Boltzmann tells us that the internal microscopic kinetic energy is
where is a constant.

## Slide 17
Boltzmann-Maxwell distribution of speed
16
If we consider that each particle individually possesses a velocity according to an indivually indeterminate probability law, the central limit theorem tells us that the process obeys the Gaussian normal law.
For a perfect gas, the problem is governed by Maxwell equilibrium distribution:

## Slide 18
Boltzmann equation
16
The probability to find a particle moving with velocity at the position at time is given by the distribution function
At low Mach number and in absence of collision, the differential of is conserved:
The Taylor development leads to
In presence of collision, this must account for the variations of probability distribution:
The collision operator can be written as the relaxation to a local equilibrium (Bhatnagar-Gross-Krook [BGK] approximation):

## Slide 19
Discrete Boltzmann equation
16
We need to solve numerically
by discretising space, time and particle velocity:
where
Macroscopic variables are obtained as

## Slide 20
printf(“ Questions? ”);
if(question)
if(haveAnswer)
giveAnswer();
else
pretendTheQuestionIsIllPosed();
end
else
printf(“ Thank you! ”);
end
Thanks for your attention!